## Slide 1: ECE369 LABS1-3

## Slide 2: InstructionFetchUnit
ProgramCounter
  A register that stores current instruction address.
  POSEDGE clocked.
PCAdder
  Output <= Input + 4.
  Increment to next instruction (similar to next line of code).
InstructionMemory
  Stores all the instructions in binary.
  Read only.
  Addressed by ProgramCounter

## Slide 3: InstructionFetchUnit
InstructionMemory
PCAdder
ProgramCounter
PCResult [31:0]
Instruction[31:0]
PCAddResult [31:0]
Rst
Clk

## Slide 4: Top
InstructionFetchUnit
Instruction[31:0]
Clk
Rst
ClkDiv
Two4DigitDisply
Instruction[15:0]
NumberA
NumberB
Instruction[31:16]
This datapath shows the top level design when implementing the InstructionFetchUnit on the FPGA. It requires clock divider and two4digit display components that are provided with the Lab1-3 packet. This is not required for Lab1-3.

## Slide 5: Is there a difference between the behavioral simulation (testbench) and post routing simulation
Post routing simulation corresponds to post-implementation functional simulation. This is the simulation of your design on chosen FPGA platform. If your design works on this then it is most likely to work on FPGA.
Behavioral: It simulates your code (more c like runs) but does not guarantee that your design will be synthesizable into RTL.
We care about synthesizable codes in this course.

## Slide 6: Why does the first instruction remain at zero for more than one clock cycle. My behavioral waveform does not have this issue.
The clock speed that set in your test bench may be too fast. Look at the line in your test bench where you're setting up your clock speed and try increasing. Note that this may also mean you have to increase the value of some wait statements in the rest of your test bench code (i.e. the amount of time to wait before setting Reset back to 0.)
Issue is that there's some setup that's happening at the start of the simulation, which cannot be completed within one clock cycle (using the faster speed) and once the setup is done it can handle the faster clock speed.

## Slide 7: I read on a few sites that for loops should be avoided in RTL design, because they are costly in terms of resources of the FPGA to implement. Is this true, should I use a for loop to instantiate the memory elements in Instruction Memory?
In RTL designs, if you use loops then it should be of definite iterations. This is because loops are converted into combinational circuits. So, during compilation, compiler should know how many iterations are there.
For memory initialization you can use "for loops". But sometimes when memory is big you might want to look into using "readmemh or readmemb", it reduces compilation time.

## Slide 8: I might be missing something, but there doesn't appear to be a lab 1-3 dropbox on d2l to submit to. Is this an error, or are we supposed to submit to a different location than d2l?
You need to join a group first. Make sure you and your partner join the same one, and the submission box should show up
Is there something we need to do in order to join a group on D2L? Currently it wont allow me to join my partners group just select it.
There is a time limit on joining or changing groups. Also verify you're trying to join the same group as your partner did.

## Slide 9: Materials To Be Careful About
1) Improper use of blocking (=) and non blocking assignments (<=) in verilog.
Reference: You may want to review section 1- 5 in the following document. You can refer to other sections also for better understanding of RTL designing.
Refer to D2L Content/Verilog/CummingsSNUG2000SJ_NBA.pdf.
2) Difference between "wire" and "reg" data type:
D2L Content/Verilog/Nets.pdf
"reg" data type does not mean "register" component. "reg" is just a data type used to declare variables for "always" and "initial" block.